Feasibility of neutron asymmetry
measurements with NICA MPD
K.Mikhaylov, O.Rogachevsky

---
Chiral Vortaic Effect
For estimation of the CVE we could explore three-particle correlator of azimuthal angels :
        <cos(φa + φb - 2φc)> ,
φa φb azimuthal angles of neutrons from midrapidiry |η|<3,
φc azimuthal angles of neutrons from high-rapidity |η|>3

---
Neutron detectors in MPD
|η|<1 (Ecal, NDet)
2<|η|<3
LAND
ring
|η|>3 (ZDC)

---
The Large Area Neutron Detector (LAND at GSI)
NIM B 240(2005)863–870: Neutron yields from
1 GeV/nucleon 238U ion beams on Fe target
O. Yordanov, K. Gunzert-Marx, P. Adrich, T. Aumann, K. Boretzky,H. Emling, G. Fehrenbacher, F. Gutermuth, H. Iwase, H. Johansson,
K.L. Jones, A. Kovalov, T. Radon, D. Schardt
LAND was designed to measure the momenta of high-energy neutrons with high efficiency; during the past decade it served in many experiments aiming at nuclear reaction and nuclear structure studies.
LAND is built from 200 modules, each of 0.1 m x· 2 m cross section and 10 cm depth and consists of alternating layers (5 mm thickness) of iron and organic scintillator material.
The intrinsic time resolution amounts to σt ≈ 250 ps; the position resolution derived from the timing signals amounts to σpos ≈ 3 cm, while the position uncertainty with respect to the other two coordinates is given by the geometry of the modules.

---
MPD with neutron detectors
“LAND”:
~1 m width
200 layers scint.+iron
Z position at 7.5m
Radius ~ 2m
Ecal or NDet
LAND Right
LAND Left

---
Simulation: software and input
MPD ROOT (from svn) simulations (Fedora 12 OS in ITEP)
Standard geometry (Cave,Pipe,Magnet,Sts,Tpc,Tof,eTof,Strow,Cpc,Zdc)
Switch off Fsa package (forward spectrometer)
|η|<1: Ndet package (form svn)
2<|η|<3: Land package (new)
|η|>3: MC tracks only
104 UrQMD Min. Bias AuAu √s = 9 GeV events
Hand made neutron asymmetry with respect to RP

---
UrQMD 2.3

---
Pseudorapidity (UrQMD)

---
Neutron energy vs Pseudorapidity (UrQMD)

---
Neutron spectra (UrQMD)
About 28 MC neutrons per event at |η|<1 and 2<|η|<3
(efficiency and cuts is not included)

---
Asymmetry in UrQMD
<cos(φa + φb - 2φc)>
Asymmetry in UrQMD is zero ( φa + φb |η|<3 and φc |η|>3 )
High impact parameter (low neutron multiplicity) region could be a problem.

---
UrQMD + GEANT3

---
 Neutron spectra at |eta|<1
TOF cut =25 ns

---
 Neutron spectra at 2<|eta|<3
TOF cut =35 ns

---
Sources of seco neutrons |eta|<1
NDET

---
Sources of seco neut 2<|eta|<3(with ZDC)

---
Hand Made Asymmetry
φc from MC neutrons |η|>3, v2,c=0.1
`

---
Asymmetry with MPD
<cos(φa + φb - 2ΨRP)> =<cos(φa + φb - 2φc)>/v2,c , ΨRP=0, v2,c=0.1
Nprim=24 Nseco=30
Expected cos(prim+seco) ~= 0.042 (5 times),
But we have 0.031 (7 times)

---
Asymmetry vs impact parameter

---
Signal/Background vs Impact parameter

---
Signal/Background vs Nseco
<cos(φa + φb - 2ΨRP)>total/<cos(φa + φb – 2ΨRP)>prim ~ (Nprim/Ntotal)2

---
 Conclusions
There is no neutron asymmetry in UrQMD. We have to introduce some asymmetry.
There are about 11+13 primary neutrons and 13+17 secondary neutrons (|η|<3) per event
3-particle correlator decreases ~7 times due to secondary neutrons for current geometry
Background depends on centrality and the effect goes down in proportional to square of backrgound

---
Thank you for your attention!

---
Rmin=.67m
Rmax=1.9m
Z:7.5-8.5m
η=3
η=2.7
η=2.0
η=2.0

---
Hand made v2,c

---
Simple simulation. Nprim=24, Nseco=30
hand made asymmetry, v2,c=0.1

---
Rapidity Central AuAu 9 GeV

---
Asymmetry in UrQMD

---
Position sensitive neutron detector (Ndet in ITEP)
Plastic: Scintillator 96x96x128 mm3
Fiber: KYRARAY,Y-11, wavelength shift, d =1mm
Photo detector:
MRS APD & Amplifier - CPTA(Golovin)
Resolution:
   σpos ≈ 2.5 cm, σt ≈ 250 ps
        εn ~ 15%
Array for FLINT experiment 6x6=36
Array for NICA(tube r=155cm and width 15 cm) about 3000 neutron detectors